## Slide 1: IEC 61850 and 61970 OPC UA Server Development and Testing

## Slide 2: IEC 61850 and 61970 CIM
IEC 61850 and IEC 61970 type data is defined using UML (Enterprise Architect)
IEC 61850 SCL and IEC 61970 CIM instance data can be exchanged using XML
This presentation discusses how IEC 61850 and 61970 servers that expose data using OPC UA can be developed and tested using this standard UML and XML.

## Slide 3: UML vs XML
IEC 61850 UML
IEC 61850 SCL
SCL CID/SCD can be seen as an instantiation of the UML model. The SCL model (XSD) will not contain all UML types (LNs, DOs) and will also define custom XML types based on the UML types. These models can be linked via shared type names. SCD files also contain “CIMish” substation data
IEC 61970 UML
IEC 61970 CIM XML
CIM XML can be seen as an instantiation of the UML model. The CIM XML model will not contain all UML types (classes and attributes) and will typically not define custom types.

## Slide 4: Two IEC 61850 Gateway Use Cases
Existing IEC 61850 Servers
Existing Non IEC 61850 Servers
Gateway
only exposes runtime model
Gateway can expose substation configuration and relationship of custom types to UML types
MMS used to expose IEC 61850 Run-time model (SCL CID)
IEC 61850 runtime model not available
SCL CID/SCD
UML Model
OPC UA
Client
OPC UA Client
Of course these files could also be imported into both gateways

## Slide 5: OPC UA NodeSet XML
Off the shelf OPC UA Server toolkits such as OpenOPCUA and Softing load OPC UA NodeSet XML files to configure their type and instance data
  IEC 61850 and IEC 61970 specific service behavior must be coded by a developer
OPC UA NodeSet XML type data can be derived from IEC 61850 or 61970 UML or a subset can be reverse engineered from an IEC 61850 SCL XML or an IEC 61970 CIM XML file

## Slide 6: OPC Foundation CTT
The OPC Foundation (OPCF) provides a Compliance Test Tool (CTT) to corporate members free of charge.
CTT test scripts can be automatically generated from a OPC UA type model by the OPCF Test Script Generator
CTT scripts test a server’s compliance with IEC 61850 8-2 or IEC 61970 502-8:
  OPC UA type model
  OPC UA service behavior

## Slide 7: OPCF CTT

## Slide 8: Developing OPC UA Test Scripts and Servers
NodeSet XML with instances (and SCL (custom) type info)
NodeSet XML with types only
OPCF Test Script
Gen
Off the shelf
Server Toolkit
IEC 61850 or 61970 UML
Contains type data only
Offis UMLbaT (EA tool plug-in)
UMLbaT GUI can provide integrated environment to manage NodeSet files and test scripts
Vendor
Is there only one way to do this? Can we achieve testability without an SCL to NodeSet mapping spec?
Provided by the OPCF

## Slide 9: Developing OPC UA Test Scripts and Servers
NodeSet XML with instances (and SCL (custom) type info)
NodeSet XML with types only
OPCF Test Script
Gen
Off the shelf
Server Toolkit
HQ/GCS XSL
Transform
SCL
CID/SCD or CIM XML
Contains instance data (SCL types are reverse engineered)
IEC 61850 or 61970 UML
Contains type data only
Offis UMLbaT (EA tool plug-in)
UMLbaT GUI can provide integrated environment to manage NodeSet files and test scripts

## Slide 10: Developing OPC UA Test Scripts and Servers
NodeSet XML with types only
OPCF Test Script
Gen
CAS Model Designer
IEC 61850 or 61970 UML
Contains type data only
Offis UMLbaT (EA tool plug-in)
UA companion spec outline

## Slide 11: Developing OPC UA Test Scripts and Servers
NodeSet XML with instances (and SCL (custom) type info)
OPCF Test Script
Gen
Off the shelf
Server Toolkit
HQ/GCS XSL
Transform
SCL
CID/SCD or CIM XML
Contains instance data (SCL types are reverse engineered)

## Slide 12: Creating OPC UA NodeSet XML and CTT Test Scripts
NodeSet XML with instances (and a subset of type info from SCL XML)
NodeSet XML with types only from UML
Test Script
Gen
Off the Shelf Server Toolkit
Compliance
TestTool
Server
TEST